# Harbor Freight   7X10 Mini Lathe   Model  39916

## For technical questions & replacement parts    1-800-444-3353

Page 5 . . .

Make sure the power switch is in the OFF position.

WARNING:  adjust the speed control knob by turning it to ZERO. BEFORE turning on the mini lathe each time it is to be used, this speed control knob must be at ZERO.  Turn the direction switch either to Forward or Reverse as desired.  Plug in the electrical cord.  Turn the power switch to the ON position to start the Lathe.  ( You MAY have to press the white START button )  Let the lathe run for about 3 minutes to determine that the Lathe is running normally.  Raise the speed gradually as needed.  To turn the Lathe off, set the Power switch to the OFF position.

WARNING:  The Mini Lathe must be completely stopped before changing Forward/Reverse direction.  Before changing gears, make sure the machine is not running.  The L position is the LOW gear, and the H position is the HIGH gear.

If an overload occurs during running of the machine, the machine will turn OFF.

If this occurs, Push the White RESET button to restart the Lathe.

(Actually- Check your tooling, Turn the Speed dial to ZERO, and press the START button)

NOTE:  This machine is equipped with a protective device which limits the depth of feed. ( Depth of CUT ? ) When the main spindle is turning at 400 RPM in the bottom gear ( LOW ), the depth of feed must be within 0.1”.  When the spindle id turning at 1000 RPM in the top gear ( High ), the depth of feed must be within 0.079”.  If the depth of feed goes beyond the mentioned limits, the protective device will cut off the electricity supply.

#33916				Rev 12/99					Page 5